# SNOL 7,2/1100 LSC01

High accuracy electric furnace with solid ceramic chamber SNOL 7.2/1100 is intended for hardening, loosening, normalizing and other thermal processing up to 1100°C. To eliminate gasses or smokes that are released during thermal processing, exhaust system may be additionally installed in the products. The furnace is excellent fit for scientific laboratories, educational institutions, medicine and industry.

#### BASIC MODEL

- Solid ceramic chamber,

- Partially exposed heating elements in four sides around a chamber,

- Outside casing in metal sheet, powder painting grey,

- Door opens sided,

- Door safety switch,

- Control panel is placed in under part of the furnace,

- Microprocessor – temperature controller,

- Ceramic bottom plate,

- Low electric power usage,

- High temperature inertness,

- High degree of accuracy.

#### OPTIONS

- Process observation window (o 35 mm) up to 1100 °C

- Fan-assisted chimney for forced air extraction

- Additional ceramic hearth plates

- Buzzer

- Digital timer

- Protection against overheating

- Data recorder

- RS232/RS-485/USB interface

- Calibration of temperature measurement

- System

- Table for supporting the furnace

- Additional 1 year guarantee

## Specification

| Technical data | Dimension | SNOL 7,2/1100 LSC01 |
| --- | --- | --- |
| Useful volume | Liter | 7,2 |
| Rated power not more than | kW | 3,3 |
| Rated supply voltage | V | 230 |
| Rated frequency | Hz | 50 |
| Number of phases | - | 1 |
| Continuous operating temperature | °C | T+10-1100 |
| Maximum temperature | °C | 1100 |
| Working chamber material | - | Ceramic |
| Maximum heating- up time (without charge) | Min. | 150 |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than | ± °C | 1 |
| Temperature uniformity in working space at rated temperature in thermal steady state without charge not more than | ±°C | 10 |
| Furnace working chamber dimensions: |
| width | mm | 195 |
| depth | mm | 295 |
| height | mm | 120 |
| Furnace external dimensions: |
| width | mm | 445 |
| depth | mm | 590 |
| height | mm | 525 |
| Mass | kg | 50 |