# SNOL 3/1100 LHM01

High accuracy electric muffle furnace SNOL 3/1100 is a universal laboratory furnace, firing up to 1100°C and designed for material testing and heat treatment such as hardening, loosening, normalising ceramic and stoneware samples. To eliminate gases or smokes that are released during thermal processing, an exhaust system may be additionally installed in the product. The furnace is an excellent fit for scientific laboratories, educational institutions, ceramic studios, medicine and industry.

#### BASIC MODEL

- One piece high thermal efficiency vacuumed ceramic fiber chamber;

- Heating elements are embedded in vacuum-formed fiber on four sides of the chamber;

- Outside casing – metal sheet, powder painting grey;

- Door opens upwards;

- Door safety interlock switch;

- Control panel is placed in the underpart of the furnace;

- Microprocessor – temperature controller;

- Ceramic bottom plate;

- Fast heating time due to low thermal mass construction;

- Low power consumption;

- Good stability and uniformity.

#### OPTIONS

- Process observation window (o 35 mm) up to 1100 °C;

- Fan-assisted chimney for air extraction;

- Additional ceramic hearth plates;

- Buzzer;

- Digital timer;

- Protection against overheating;

- Data recorder;

- RS232/RS-485/USB interface;

- Calibration of temperature measurement system;

- Table for supporting the furnace;

- Protective gas atmosphere;

- Gas box up to 1100 °C;

- Metal tray;

- Additional 1 year guarantee.

## Specification

| Technical data | Dimensions | SNOL 3/1100 LHM01 |
| --- | --- | --- |
| Useful volume | Liters | 3 |
| Rated power not more than | kW | 1.7 |
| Rated supply voltage | V | 230 |
| Rated frequency | Hz | 50 |
| Number of phases | - | 1 |
| Continuous operating temperature | °C | T+10-1100 |
| Maximum temperature | °C | 1100 |
| Working chamber material | - | Fiber muffle |
| Maximum heating- up time (without charge) | Min. | 35 |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than | ± °C | 1 |
| Temperature uniformity in working space at rated temperature in thermal steady state without charge not more than | ±°C | 10 |
| Furnace working chamber dimensions: |
| width mm | mm | 120 |
| depth mm | mm | 200 |
| height mm | mm | 105 |
| Furnace external dimensions: |
| width mm | mm | 345 |
| depth mm | mm | 470 |
| height mm | mm | 430 |
| Mass | kg | 17 |