# SNOL 60/300 LSN11

A new laboratory oven SNOL 60/300 is designed for thermal treatment of various materials up to 300°C. This electric oven is designed for treatments such as drying, heating, thermal testing, aging and similar purposes in an airflow environment. Forced air convection allows a homogeneous temperature distribution during the process, which ensures optimal results, moreover, good technical parameters ensure high-quality results. This oven is also available in economical version LSN41 (without buzzer and airflow speed controller). The oven can be used in scientific laboratories, educational institutions, medicine and industry.

#### BASIC MODEL

- Control panel is placed in the underpart of the oven;

- Ventilation motor on back side;

- Forced horizontal air circulation;

- Inside casing – 304 stainless steel;

- 3 stainless steel shelves;

- Outside casing – metal sheet, powder painting (grey);

- Insulation – rock wool (complete lack of asbestos);

- Door opening to the right, inner door in stainless steel, silicon joint;

- OTP (over temperature protection);

- Microprocessor – temperature controller;

- Air fan speed controller;

- Buzzer;

- Low electric power usage for increased energy efficiency;

- Short heating up / cooling down period.

#### OPTIONS

- Economical version (Ec) without fan speed controller and buzzer;

- Additional shelves;

- Reinforced shelves;

- Metal tray;

- Digital timer;

- RS232/RS-485/USB interface;

- Calibration of temperature;

- Measurement system;

- Furnace exterior made from stainless steel;

- Table for supporting the furnace;

- Process observation window.

## Specification

| Technical data | Dimensions | SNOL 60/300 LSN11 |
| --- | --- | --- |
| Useful volume | Liters | 60 |
| Rated power not more than | kW | 2 |
| Rated supply voltage | V | 230 |
| Rated frequency | Hz | 50 |
| Number of phases | - | 1 |
| Continuous operating temperature | °C | T+10-300 |
| Maximum temperature | °C | 300 |
| Working chamber material | - | st.steel |
| Working chamber surroundings | - | air (with hot air fan) |
| Airflow |  | horizontal |
| Shelves (number)/max. |  | 3/7 |
| Maximum heating- up time (without charge) up to 300°C | Min. | 34 |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than | ± °C | 0,3 |
| Temperature uniformity in working space at 300°C temperature in thermal steady state without charge not more than | ±°C | 2,0 |
| Oven working chamber dimensions: |  |  |
| width | mm | 380 |
| depth | mm | 380 |
| height | mm | 420 |
| Outside dimensions: |  |  |
| width | mm | 600 |
| depth | mm | 755 |
| height | mm | 720 |
| Mass | kg | 49 |