# SNOL 67/350 LSN01

Economical low temperature oven SNOL 67/350 is designed for thermal treatment such as drying, heating, thermal testing, aging and similar purposes in natural air-flow environment up to 350°C. Good technical parameters ensure to high-quality results. This oven can be used in scientific laboratories, educational institutions, medicine and industry.

#### BASIC MODEL

- Control panel is placed on the left side,

- Natural air convection without air fan,

- 304 stainless steel,

- 3 shelves,

- Outside casing in metal sheet, powder painting grey,

- Insulation rock wool (complete lack of asbestos),

- Door opening on the right, inner door in stainless steel, silicon joint,

- Microprocessor – temperature controller,

- Low electric power usage for increased energy efficiency,

- Short heating up / cooling down period.

#### OPTIONS

- Additional shelves

- Reinforced shelves

- Metal tray

- Digital timer

- Buzzer

- Over-temperature protection

- Data recorder

- RS232/RS-485/USB interface

- Calibration of temperature measurement system

- Oven exterior made of stainless steel

- Stand for supporting the oven

- Additional 1 year guarantee

## Specification

| Technical data | Dimension | SNOL 67/350 LSN01 |
| --- | --- | --- |
| Useful volume | Liter | 67 |
| Rated power not more than | kW | 2 |
| Rated supply voltage | V | 230 |
| Rated frequency | Hz | 50 |
| Number of phases | - | 1 |
| Continuous operating temperature | °C | T+10-350 |
| Maximum temperature | °C | 350 |
| Working chamber surroundings | - | air (without hot air fan) |
| Airflow |  | natural |
| Shelves (number)/max. |  | 3/7 |
| Maximum heating- up time (without charge) up to 350°C | Min. | 40 |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than | ± °C | 2 |
| Temperature uniformity in working space at 350°C temperature in thermal steady state without charge not more than | ±°C | 14 |
| Oven working chamber dimensions: |  |  |
| width | mm | 390 |
| depth | mm | 445 |
| height | mm | 390 |
| Outside dimensions: |  |  |
| width | mm | 670 |
| depth | mm | 615 |
| height | mm | 580 |
| Mass | kg | 37 |