# SNOL 420/300 LSN11

A new laboratory oven SNOL 420/300 is designed for thermal treatment of various materials up to 300°C. This electric oven is designed for treatments such as drying, heating, thermal testing, aging and similar purposes in an airflow environment. Forced air convection allows a homogenous temperature distribution during all process, which ensures optimal results as well as good technical parameters ensure high-quality results. This oven is also available in economical version LSN41 (without buzzer and airflow speed controller). The oven can be used in scientific laboratories, educational institutions, medicine and industry.

#### BASIC MODEL

- Control panel is placed in under part of the oven;

- Ventilation motor on back side;

- Forced horizontal air circulation;

- Inside casing – 304 stainless steel;

- 3 stainless steel shelves;

- Outside casing – metal sheet, powder painting grey;

- Insulation – rock wool (complete lack of asbestos);

- Two doors, inner doors in stainless steel, silicon joint;

- OTP (over temperature protection);

- Microprocessor – temperature controller;

- Air fan speed controller;

- Buzzer;

- Low electric power usage for increased energy efficiency;

- Short heating up / cooling down period.

#### OPTIONS

- Economical version (Ec) without fan speed controller and buzzer;

- Additional shelves;

- Reinforced shelves;

- Metal tray;

- Digital timer;

- RS232/RS-485/USB interface;

- Calibration of temperature;

- Measurement system;

- Furnace exterior made of stainless steel;

- Table for supporting the furnace;

- Process observation window.

## Specification

| Technical data | Dimensions | SNOL 420/300 LSN11 |  |
| --- | --- | --- | --- |
| Useful volume | Liters | 420 |  |
| Rated power not more than | kW | 6,2 |  |
| Rated supply voltage | V | 400 |  |
| Rated frequency | Hz | 50 |  |
| Number of phases | - | 3 |  |
| Continuous operating temperature | °C | T+10-300 |  |
| Maximum temperature | °C | 300 |  |
| Working chamber material | - | st.steel |  |
| Working chamber surroundings | - | air (with hot air fan) |  |
| Airflow |  | horizontal |  |
| Shelves (number)/max. |  | 3/7 |  |
| Maximum heating- up time (without charge) up to 300°C | Min. | 40 |  |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than | ± °C | 1 |  |
| Temperature uniformity in working space at 300°C temperature in thermal steady state without charge not more than | ±°C | 9 |  |
| Oven working chamber dimensions: |  |  |  |
| width | mm | 1000 |  |
| depth | mm | 500 |  |
| height | mm | 860 |  |
| Outside dimensions: |  |  |  |
| width | mm | 1200 |  |
| depth | mm | 905 |  |
| height | mm | 1200 |  |
| Mass | kg | 178 |  |