# SNOL 0,25/1250 LXC04

High temperature horizontal electric tube furnace SNOL 0.25/1250 is designed for materials heat treatment up to 1250◦C. This model is reliable with robust ceramic chamber (tube). Furnace equipped with covers of tubes. Furnace can be used in laboratories, medicine, educational institutions, and industry.

#### BASIC MODEL

- Ceramic tube chamber

- Microprocessor-controlled thermoregulator

- High-quality, ecological thermal insulation material

- Low electric power consumption

- Short heating up/cooling down period

- High degree of accuracy

- Exterior painted with powder coating (RAL 7035)

- 1 year guarantee

#### OPTIONS

- Buzzer

- Digital timer

- Protection against overheating

- Data recorder

- RS232/RS-485/USB interface

- Calibration of temperature measurement system

- Table for supporting the furnace

- Additional 1 year guarantee

## Specification

| Technical data | Dimension | SNOL 0,25/1250 LXC04 |
| --- | --- | --- |
| Useful volume | Liter | 0,19 |
| Rated power not more then, kW | kW | 3,7 |
| Rated supply voltage, V | Volt | 230 |
| Rated frequency, Hz | Hz | 50 |
| Number of phases | - | 1 |
| Continuous operating temperature °C | °C | 1250 |
| Maximum temperature | °C | 1250 |
| Working chamber material | - | Ceramic |
| Working chamber surroundings | - | air |
| Maximum heating- up time (without charge), min | Min. | 50 |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than ± °C | ± °C | 1 |
| Temperature uniformity in working space at rated temperature in thermal steady state without charge not more than ± °C | ±°C | 10 |
| Furnace working chamber dimensions: |  |  |
| Depth mm | mm | 200 |
| Diameter mm | mm | 35 |
| Furnace dimensions: |  |  |
| width mm | mm | 675 |
| depth mm | mm | 545 |
| height mm | mm | 565 |
| Mass netto | kg | 38 |