# SNOL 30/1300 LSF01

High accuracy electric fiber-insulated chamber furnace SNOL 30/1300 is universal laboratory furnace, designed for materials testing, heat treatment such as hardening, loosening, normalising, ceramic and stoneware samples firing up to 1300°C. To eliminate gasses or smokes that are released during thermal processing, exhaust system may be additionally installed in the products. The furnace is excellent fit for scientific laboratories, educational institutions, ceramic studios, medicine and industry.

#### BASIC MODEL

- Chamber made of fiber thermal insulation plates,

- Heating elements wrapped on tubes in two sides of the chamber,

- Outside casing in metal sheet, powder painting grey,

- Door opens to the right side,

- Door safety interlock switch,

- Control panel is placed in under part of the furnace,

- Microprocessor – temperature controller,

- Ceramic bottom plates,

- Fast heating time due to low thermal mass construction,

- Low power consumption,

- Good stability and uniformity.

#### OPTIONS

- Fan-assisted chimney for forced air extraction

- Additional ceramic bottom plates

- Buzzer

- Digital timer

- Protection against overheating

- Data recorder

- RS232/RS-485/USB interface

- Calibration of temperature measurement system

- Table for supporting the furnace

- Protective gas atmosphere

- Metal tray

## Specification

| Technical data | Dimension | SNOL 30/1300 LSF01 |
| --- | --- | --- |
| Useful volume | Liter | 30 |
| Rated power not more than | kW | 4.6 |
| Rated supply voltage | V | 230 |
| Rated frequency | Hz | 50 |
| Number of phases | - | 1 |
| Continuous operating temperature | °C | T+10-1300 |
| Maximum temperature | °C | 1300 |
| Working chamber material | - | Fiber plates |
| Maximum heating- up time (without charge) | Min. | 150 |
| Temperature stability in working chamber at rated temperature in thermal steady state without charge not more than | ± °C | 1 |
| Temperature uniformity in working space at rated temperature in thermal steady state without charge not more than | ±°C | 10 |
| Furnace working chamber dimensions: |
| width | mm | 200 |
| depth | mm | 440 |
| height | mm | 290 |
| Furnace external dimensions: |
| width | mm | 640 |
| depth | mm | 870 |
| height | mm | 840 |
| Mass | kg | 120 |